## Slide 1: Detection and Monitoring Intra/Inter Crosstalk in Optical Network on Chip
Dr. Ahmed Jedidi
Assistant Professor / Chairperson of computer Engineering Department
College of Engineering Ahlia University Bahrain
ajedidi@ahlia.edu.bh

## Slide 2: What are we going to talk about today?

## Slide 3
You know what, …
Why are multiprocessor architectures more and more popular?
Network on Chip Trend (NoC)
Crosstalk in optical communication
Detection and monitoring Crosstalk noise in ONoC

## Slide 4: New Challenges :
Technology progress:
  Nbr transistors & density
Moore’s Law (Gordon Moore – 1965) “The complexity for minimum component costs has increased at a rate of roughly a factor of two per year

## Slide 5: New Challenges :
Embedded Applications ++ complex and varied.
  Need a performing HW.
  Reduce consumption energy
  HW/SW Design, implementation and verification simple
  (Time to Market)

## Slide 6: Solution : Multiply processors
Better use of transistors.
  Reuse unit.
Extensibility
  Add new cores
Optimization HW/SW

## Slide 7: Multiprocessors…my grandfather told me the story…
MPSoC different than the classic multiprocessor architectures:
  1 chip = Processors, Caches, Noc, FPGA, …
  New models of programming
"Don’t be encumbered by past history, go off and do something wonderful"
Robert Noyce, co-fondateur d'Intel Corp.

## Slide 8: MPSoC Chalenges: Number of PEs

## Slide 9: Typical MPSoC Architecture
Network-On-Chip
Core+cache
Core+cache
HW accelerator (FP, FFT, JPEG, ..)
Reconfigurable Logic
Memory Unit
(DRAM, SRAM, SPR, ..)
Memory Unit
(DRAM, SRAM, SPR, ..)
I/O
USB, BT, CAN
I/O
USB, BT, CAN
I/O
USB, BT, CAN…

## Slide 10: Energy Efficiency
Need for efficiency (power + energy):
„Power is considered as the most important constraint in embedded systems“ [in: L. Eggermont (ed): Embedded Systems Roadmap 2002, STW]
Why worry about energy and power?

## Slide 11: Low Power vs. Low Energy Consumption
  Minimizing the power consumption is important for
    the design of the power supply
    the design of voltage regulators
    the dimensioning of interconnect
    short term cooling
  Minimizing the energy consumption is important due to
    restricted availability of energy (mobile systems)
      limited battery capacities (only slowly improving)
      very high costs of energy (solar panels, in space)
    cooling
      high costs
      limited space
    dependability
    long lifetimes, low temperatures

## Slide 12
Energy consumption== Temperature:
  High temperature :
    Decrease the performance
    Cause breakdowns
    Decrease Mean Time To Failure «MTTF
Decreasing the temperature increases the life of the Chip
Thermal Dissipation

## Slide 13: Thermal & Power Modeling
task
task
task
Modello
Termico
Tj
Thermal
model
Tn,j
Pn,j
Modello di
potenza
Taskj
Pj
Power model
P=g(task,f)

## Slide 14: Network On-Chip Communications
Growing number of cores  Networks-on-Chip (NoC)
Shared, packet-switched, optimized for communications
  Resource efficiency
  Design simplicity
  IP reusability
  High performance
But no true relief in power dissipation
IBM Cell ~30-50% of chip power budget allocated to global interconnect

## Slide 15: Network On-Chip Communications
Modern Processors contain multiple cores integrated into a single chip
Hundreds of cores on a single chip will soon be possible due to Technology Scaling
On-chip Communication Networks that connect the cores (commonly called Network-on-Chips or NoCs) are becoming critical components in such processors
(Source: http://sips.inesc-id.pt/~nfvr/msc_theses/msc12ac/)
Reference:
N. E. Jerger and L.-S. Peh, "On-chip networks," Synthesis Lectures on Computer Architecture, vol. 4, no. 1, pp. 1–141, Jan. 2009.

## Slide 16
Metrics for judgement of NoCs :
Bandwidth Density
Energy Efficiency
Latency
Scalability

## Slide 17: Why Photonics?
TX
RX
ELECTRONICS:
Buffer, receive and re-transmit at every router.
Each bus lane routed independently. (P  NLANES)
Photonics changes the rules for Bandwidth-per-Watt.
Photonics:
Modulate/receive ultra-high bandwidth data stream once per communication event.
Broadband switch routes entire multi-wavelength stream.
RX
TX
RX
RX
TX
RX
TX
RX
TX
TX

## Slide 18: Photonics in computing system today
Optical link
• Uses monolithic integration that reduces energy consumption
• Utilizes the standard bulk CMOS flow
• Cladding is used to increase the total internal reflection  reduces data loss

## Slide 19: Photonics in computing system today
WDM, DWDM
Supports WDM that improves bandwidth density
DWDM can transports tens to hundreds of wavelengths per fiber.
Integrated Tb/s optical link on a single chip is ongoing

## Slide 20: MPSoC Vision

## Slide 21: Silicon Photonic Integration
MIT, 2008
IBM, 2007
Cornell, 2005
Luxtera, 2005
UCSB, 2006

## Slide 22: Basic Optical Devices
The crossing switching element (CSE).
The parallel switching element (PSE)
Micro-Resonator (MRs)

## Slide 23: Crosstalk noise in basic devices
=

## Slide 24: Crosstalk noise in ONoC

## Slide 25: Crosstalk Detection and monitoring

## Slide 26: Crosstalk Detection and monitoring
Imperment Alarm | Description
No Crosstalk | No detection of crosstalk (healthy signal)
Acceptable Crosstalk | 
Dangenrous Crosstalk | OR
Imperment Alarm | Description
No Crosstalk | No detection of crosstalk (healthy signal)
Acceptable Crosstalk | 
Dangenrous Crosstalk | 

## Slide 27: Crosstalk Detection and monitoring
Algorithm 1. Crosstalk noise Monitoring
FOR ʎi=1 to 32 IF (Crosstalk detection = 1) Then IF () Then Imperment Alarm = Dangerous Crosstalk Else IF () Then Imperment Alarm = Dangerous Crosstalk Else IF () Then Imperment Alarm = Acceptable Crosstalk END IF Else IF (Crosstalk detection = 0) Then Imperment Alarm = No Crosstalk END IF END FOR
Algorithm 1. Crosstalk noise Monitoring

## Slide 28: Crosstalk Detection and monitoring

## Slide 29: Crosstalk Detection and monitoring

## Slide 30: Crosstalk Detection and monitoring

## Slide 31: Conclusion:
MPSoC is one of the solution to satisfy the performance required by the new embedded applications .
Network on Chip is one of the problem of MPSoC
Optical Network on Chip promising a solution for the new MPSoC
Crosstalk noise one of the serious problem in ONoC
Detection and monitor crosstalk noise is indispensable to guarantee high performance for MPSoC